## Slide 1: Solid Phase Extraction Optimization Experiment

## Slide 2: Standard solution of Compounds of Interest and Required Components
Make a 5 mg/mL solution of compounds
Dilute 5 mg/mL compound solution with water to yield a 50 ug/mL stock solution, experiment requires very low organic content
Required solvents: Methanol, di water
Collection tubes, 5 mL or larger collection tube volume
Required pipettes: 1 mL and 5 mL
SPE 10 port manifold
Required SPE material: Agilent Bond Elut C18 500 mg/6 mL p/n: 12102052 or C18 100 mg/3 mL p/n: 12102099 will need 20 SPE cartridges to accomplish both the low and high pH experiment
  HPLC for analysis

## Slide 3: Generic Procedure for Optimization
Place 10 SPE cartridges on SPE manifold, one SPE cartridge per port, 10 port manifold; for low pH and then repeat procedure for high pH experiments
Procedure shown below is for a 500 mg/6 mL SPE cartridge (if a 100 mg/3 mL SPE cartridge is used instead change all volumes to 1 mL)
Condition 1-10 SPE cartridges: 3 mL methanol, then 3 mL water
Load 1-10 SPE cartridges: 3 mL of 50 ug/ml stock solution
Place collection tubes under every SPE cartridge prior to addition of wash solution
Wash Individual SPE cartridge: 3 mL of pH wash solutions
Collect each wash solution from individual SPE cartridge, analyze by HPLC

## Slide 4: General Overall Steps: Determine Recovery for Each Wash
Perform condition, equilibrate and load steps on twenty cartridges
    As per generic method
    Standards, not real samples
Wash each cartridge with one of the twenty prepared wash solutions
No final elution step
Dry down and reconstitute in mobile phase
    Add ISTD if needed
    Necessary for % recovery data
Calculate recoveries for each sample

## Slide 5: Information to be Determined from Optimization Experiment SPE used: Bond Elut C18, 500 mg/6 mL p/n: 12102052
Condition – 3 mL MeOH
Equilibrate – 3 mL H20
Load – 3 mL sample
Wash – 3 mL 5% MeOH
Elute – 3 mL MeOH
Condition – 3 mL MeOH
Equilibrate – 3 mL H2O
Load – 3 mL sample
Wash 1 – ??????
Elute – ??????
Generic extraction
Optimized extraction

## Slide 6: Employing Systematic SPE Method Development
SPE method development approach offers a simple and highly selective extraction method
When compared to a generic method using C18 phase, the systematic SPE method development approach provided an optimum method
Results will provide optimized wash and elution conditions for compounds of interest, namely:
    Wash: appropriate pH and highest percentage of organic without eluting compounds of interest, maximum removal of interferences
    Elute: appropriate pH and lowest percentage of organic that elutes compounds of interest
Possibly eliminating the final SPE eluate evaporation and reconstitution steps typical of most reversed-phase SPE procedures

## Slide 7: Prepare Low pH Washes
2% FA
0%
MeOH
10%
MeOH
20%
MeOH
30%
MeOH
40%
MeOH
50%
MeOH
60%
MeOH
70%
MeOH
80%
MeOH
90%
MeOH

## Slide 8: Prepare High pH Washes
0%
MeOH
10%
MeOH
20%
MeOH
30%
MeOH
40%
MeOH
50%
MeOH
60%
MeOH
70%
MeOH
80%
MeOH
90%
MeOH
5%
NH4OH

## Slide 9: Structure: Atenolol used as an example
pKa 9.6, base

## Slide 10: Example: Low pH (2% formic acid in eluent) Atenolol / Bond Elut C18
40% organic elution
40%
Observe elution of compound from SPE cartridge by 10% organic with low pH, washing cartridge to remove interferences will effect compound recovery, wash and elution window extremely narrow
Notes: Ben can you change the axis to 0, 10, 20%... 70%, etc on these?

## Slide 11: Example: High pH (5% NH4OH in eluent) Atenolol / Bond Elut C18
25% organic wash
55% organic elution
55%
25%
Observe much larger wash and elution window for the compound offering optimum wash and elution conditions

## Slide 12: Optimized Extraction Scheme – Atenolol (example) Bond Elut C18, 500 mg/6 mL
Condition – 3 mL MeOH
Equilibrate – 3 mL H20
Load – 3 mL sample
Wash – 3 mL 5% MeOH
Elute – 3 mL MeOH
Condition – 3 mL MeOH
Equilibrate – 3 mL H2O
Load – 3 mL sample
Wash 1 – 3 mL 25% MeOH (5%NH4OH)
Elute – 3 mL 55% MeOH (5%NH4OH)
Compound eluted as free base
Generic extraction
Optimized extraction